## Slide 1
PROJECT
Linux Kernel Netfilter
Code Analysis and Improvement
Team 3
Performance Optimization by Resolving Connection Tracking Lock Contention

## Slide 2
Contents
2.
3.
4.
5.
Netfilter Architecture
Packet Processing Flow
nf_hook_slow Analysis
Connection Tracking Overview
6.
Processing Existing & New Connections
7.
Problem: Lock Contention
1.
Project Overview
9.
10.
11.
12.
Improvement 2: Per-Bucket Lock
Performance Analysis Environment
Results: Dynamic Spinlock
Results: Per-Bucket Lock
13.
Result Comparison & Analysis
14.
Conclusion
8.
Improvement 1: Dynamic Spinlock

## Slide 3
  Detailed analysis of the Netfilter/Connection Tracking code path.
  Improve performance in high-load environments by minimizing lock contention.
  In high-load environments, accessing the nf_conntrack hash table causes network throughput degradation due to lock contention.
  Need to analyze the bottleneck of the existing global lock array method.
Research Background
Research Goal:
Project Overview
Key Contributions:
Analysis : Detailed analysis of the NF_HOOK → nft_do_chain path and the existing/new connection processing mechanism in nf_conntrack_in.
Improvement 1 : Implemented dynamic lock array allocation based on CPU count and hash table size.
Improvement2 : Implemented dedicated locks for each hash bucket to distribute contention.
Evaluation : Quantitative performance measurement using perf and comparative analysis of the two methods.

## Slide 4
Netfilter Architecture
What is Netfilter?
Key Operating Principles:
Relation to Connection Tracking
  A packet control framework inside the Linux kernel network stack.
  Intercepts and controls traffic by placing Hooks on the main paths where packets travel.
  Hooking: Intercepting packets at key points.
  Verdict: Executes registered handler functions and decides the packet's fate (e.g., ACCEPT, DROP).
  The Connection Tracking system is a state management module that operates by registering at these Netfilter hook points.

## Slide 5
Packet Processing Flow :
NIC → ip_rcv() → NF_HOOK
  NIC Receive (L1):
  2. sk_buff Conversion (L2)
  3. Header Analysis
  4. ip_rcv() → NF_HOOK
  Network card receives packets from outside (Physical layer).
  Driver converts Ethernet frame to sk_buff structure.
  Analyzes Ethernet header to identify IP packets.
  Validates IPv4 packets and calls NF_HOOK
  5. Hook Chain Execution
  Sequentially executes hook functions: NF_Hook → nf_hook() → nf_hook_slow()

## Slide 6
Packet Processing Flow :
NIC → ip_rcv() → NF_HOOK

## Slide 7
nf_hook_slow() Analysis
ACCEPT: Packet allowed
DROP: Packet discarded
QUEUE: Sent to user space
  Proceeds to the next hook.
  Memory freed via kfree_skb(). Function exits immediately (subsequent hooks not executed).
  Handled by NFQUEUE system via nf_queue().
DEFAULT
  Exception handling for undefined verdicts.
Verdict Branching

## Slide 8
Analysis after nf_hook_slow()

## Slide 9
Connection Tracking Overview
nf_conntrack_in()
  Tuple-based Identification: Uses 5-tuple (Source IP/Port, Dest IP/Port, Protocol).
  Hash Table Search: Calculates hash using hash_conntrack_raw() and searches buckets.
  RCU Concurrency Control: Read operations are protected by RCU to minimize lock overhead.
  Protocol-specific Processing: Handles TCP state machine, UDP timeouts, etc.
Core Role:
  The entry point for Connection Tracking in Netfilter.
  Checks if a packet belongs to an existing connection and manages its state.
Key Features:
  Extract Connection Tuple from Socket Buffer (skb)
  2.Search for Existing Connection in Hash Table
  3.If Existing: Update State & Return; If New: Create & Validate Protocol
  4.Process Packet based on Protocol & Return Result
  (Source/Destination IP/Port, Protocol)
  __nf_conntrack_find_get
  TCP/UDP/ICMP, etc.
  5.Confirm and Insert into Table at Confirm Hook
  __nf_conntrack_confirm
  Key Processing Steps

## Slide 10
Connection Tracking Overview
Duplicate/Exception Handling
1
  Checks if a connection object is already attached to the packet (skb) using nf_ct_get (e.g., loopback). If present, it passes immediately.
L4 Protocol Parsing
2
  Extracts the Layer 4 protocol number (protonum, e.g., TCP, UDP) and data offset (dataoff) from the packet header
ICMP separate processing
3
  Since ICMP packets are control messages, they are handled by a separate function (handle_icmp) (e.g., checking if an error message is related to an existing connection).
Connection Identification
4
  Calls resolve_normal_ct to generate a 5-Tuple and determines whether it is an existing connection by searching (Lookup) the hash table or creating a new one.

## Slide 11
Search Result
Existing Connection Processing (Search Path)
Receives the connection tuple (Source/Dest IP, Port, Protocol) as input, calculates, and returns the hash value.
  Iterate through buckets corresponding to the hash value.
  Check status of each connection (Garbage Collection if expired).
  Return the pointer if the connection key matches.
Uses the RCU (Read-Copy-Update) locking mechanism to safely traverse buckets during concurrent access, ensuring hash table consistency.
  Buckets can change dynamically due to RCU structure.
  Performs re-lookup if bucket state change is detected.
  Allows write operations during read operations.
When an existing connection is found, increments the reference count to ensure memory safety and returns the connection pointer to perform state updates.
hash_conntrack_raw
__nf_conntrack_find
RCU Protection & Bucket Traversal
Concurrency Handling
Key Function Call Flow
  Acquire connection info via nf_ct_tuplehash_to_ctrack().
  Increment connection reference count (refcount) by 1.
  Key match success → Return connection pointer.
  Key mismatch → Restore refcount and continue searching.
__nf_conntrack_find_get

## Slide 12
Existing Connection Processing (Search Path)

## Slide 13
  Depending on the protocol of the tracked connection, individual functions are called to update the connection information corresponding to the packet.
  Each function returns its own packet processing result.
  Examples: NF_ACCEPT, NF_DROP, NF_QUEUE
Finally, the nf_conntrack_in() Function Returns the Packet Processing Result
nf_conntrack_in
Existing Connection Processing (Search Path)

## Slide 14
When the connection lookup returns NULL, it indicates a new flow, and a new conntrack entry is created
New Connection Processing (Search Path)

## Slide 15
  Creation Stage
Generate reverse tuple → Allocate memory via __nf_conntrack_alloc → Assign memory → Check helper/expectation
  Unconfirmed Stage
Add to unconfirmed_list and attach ct to skb (IP_CT_NEW)
  Validation Stage
Protocol-specific validity check (e.g., TCP SYN verification)
  Confirmation Stage
Lock table using nf_conntrack_double_lock → Remove from unconfirmed list → Insert into hash table → Set IPS_CONFIRMED
New Connection Processing (Creation & Confirmation)

## Slide 16
Allocate memory for the nf_conn structure by calling __nf_conntrack_alloc.
Temporarily register the entry into the unconfirmed list.
New Connection Processing (Search Path)

## Slide 17
Officially insert the entry into the global hash table.
Since the global table is shared across all CPUs, concurrent writes can corrupt data — therefore, a lock must be acquired.
New Connection Processing (Search Path)

## Slide 18
nf_conntrack_double_lock
New Connection Processing (Search Path)

## Slide 19
Problem - Intensified Lock Contention
Structural Imbalance
(1024 vs 65k)
nf_conntrack_
double_lock
Performance Degradation in Virtualized Environments
  The global shared lock array size is only 1,024.
  The actual number of hash buckets is much larger (e.g., 65,536).
  1024 vs 65k mismatch causes a structural bottleneck.
When calling __nf_conntrack_confirm or nf_ct_delete,
even different buckets may share the same lock index → unnecessary lock contention occurs.
Prolonged lock spinning increases Host-OS trap frequency,
leading to higher vp_notify overhead → overall system efficiency drops in virtualized environments.

## Slide 20
  CPU-based Calculation : Consider the maximum number of usable CPUs and the number of tasks they can handle. → Allocate 4 locks per CPU.
  Hash Table Size-based Calculation : Determine the number of buckets per lock based on the current hash table size. Larger hash tables result in more locks.
  Final Decision : Choose the larger value among the two above to ensure sufficient concurrency.
  Spinlock arrays are dynamically allocated during the execution of nf_conntrack_init_start().
  This removes the limitation of the fixed 1024-lock static allocation.
  The lock array size is determined based on the system environment to maximize performance.
Dynamic Allocation Timing
Factors for Determining Lock Count
Improvement 1: Dynamic Spinlock Allocation (Concept)
  Power-of-Two Adjustment
  Range Validation
  User Parameters
  Efficient Indexing
Final lock count is rounded to the nearest power of two for efficient indexing
(use bitwise AND instead of modulo for lock index calculation).
Ensure the calculated lock array size is within the predefined minimum/maximum range for stability.
If the user explicitly sets the lock array size:
Validate that it falls within the allowed range and adjust to the nearest power of two if needed.
Implement fast lock selection using: lock_index = hash & (nr_locks - 1)
Optimization Methods

## Slide 21
Determine Lock Array Size
1
  CPU count: estimate using max_possible_cpus and num_online_cpus
  Default: allocate 4 locks per CPU
  Determine number of buckets per lock based on hash table size
  Adjust the final value to the nearest power of two
  (validate within minimum/maximum bounds)
Dynamic Allocation & Initialization
2
  Allocate lock array memory according to the calculated size
  Initialize each lock with spin_lock_init()
  Update global lock array pointer and size variables
Optimization: Bitwise AND Operation
3
  lock_index = hash & (nr_locks - 1)
  Power-of-two array size → replace modulo with bit masking
  Improves performance when computing lock index from hash values
Reallocation on Resize
4
  When hash table size changes → free old lock array
  Recalculate and reallocate based on the new table size
  Replace existing lock structures and pointers accordingly
Improvement 1: Dynamic Spinlock Allocation (Details)

## Slide 22
Function to calculate lock array size
Function to allocate the lock array
  Leverage power-of-two lock array size to optimize division using bitwise AND
Improvement 1: Dynamic Spinlock Allocation (Details)

## Slide 23
Modify the hash table resize function accordingly
Replace the static allocation approach with a dynamic allocation approach
Use bitwise AND instead of modulo when deriving lock index from hash values
Improvement 1: Dynamic Spinlock Allocation (Details)

## Slide 24
New structure nf_conntrack_bucket:
  Assign an independent lock to each hash bucket to distribute lock contention.
  Replace the previous global lock array (nf_conntrack_locks, fixed at 1024 locks)
  with a structure where each bucket owns its own lock
Key Idea
Structural Design
Transition Changes
Each bucket manages its head (list) and lock (spinlock) together,
enabling isolated and fine-grained concurrency control
hlist_nulls_head
nf_conntrack_bucket
Hash table entry type changed to bucket structure
nf_conntrack_locks
nf_conntrack_hash_lock
Lock is now managed per bucket, instead of globally
nf_conntrack_hash
nf_conntrack_hash_head
Access hash table through bucket’s head
Improvement 2: Per-Bucket Lock Concept

## Slide 25
nf_conntrack_core.c
1
  Remove global lock array initialization
  Define nf_conntrack_bucket and manage both head & lock together
  Update ct_hash pointer type: hlist_nulls_head* → nf_conntrack_bucket*
  Use bucket.lock for insert/delete/lookup operations
  Remove previous lock initialization logic
nf_conntrack.h
2
  Replace hlist_nulls_head with nf_conntrack_bucket: update table element type
  Add structure definition reference for bucket-based table
nf_conntrack_netlink.c
3
  Replace lock usage: nf_conntrack_locks → bucket.lock
  Change list type: hlist_nulls_head → nf_conntrack_bucket
  When accessing hash table, use .head member in bucket
nf_conntrack_standalone.c
4
  Same lock model update: use bucket.lock
  Same list type change: use bucket structure instead of head list
  Access .head for hash lookup operations
Core Change : Remove the global lock array (nf_conntrack_locks) → each bucket owns its own lock → lock contention distributed, concurrency improved, scalability enhanced
Improvement 2: Per-Bucket Lock Details

## Slide 26
Newly define the nf_conntrack_bucket structure.
Update the type of ct_hash pointer from hlist_nulls_head to nf_conntrack_bucket.
Improvement 2: Per-Bucket Lock Details

## Slide 27
  Replace previous lock access:
nf_conntrack_locks → nf_conntrack_hash.lock (per-bucket lock)
  Replace previous hash head access:
nf_conntrack_hash → nf_conntrack_hash.head
Improvement 2: Per-Bucket Lock Details

## Slide 28
Use per-bucket locks (nf_conntrack_hash.lock) instead of the legacy global lock array (nf_conntrack_locks).
Remove initialization code related to the deprecated nf_conntrack_locks.
Improvement 2: Per-Bucket Lock Details

## Slide 29
Replace occurrences of hlist_nulls_head with nf_conntrack_bucket throughout the code.
  Replace nf_conntrack_locks with nf_conntrack_hash.lock (per-bucket lock)
  Replace hlist_nulls_head with nf_conntrack_bucket
  Update hash table access to reference the .head member of the bucket structure
Improvement 2: Per-Bucket Lock Details

## Slide 30
> Disable unnecessary module loading & automatic load balancing
> IRQ Pinning: bind virtio IRQ → CPU 0
> Reduce hash table size: buckets=512, max=300,000
> Increase timeout: udp_timeout=3600
> Disable tracking bypass (ensure all traffic is tracked)
Quantitatively evaluate lock contention mitigation by observing CPU usage changes in
__nf_conntrack_find_get and __nf_conntrack_confirm under high-load situations.
  Server Settings
Tool : perf top
option : -C 0 -F 100 (CPU 0 only, 100Hz sampling)
Timing : When nf_conntrack_count reaches 300k and the system becomes overloaded
Measurement
> Script: maintain pktgen.sh parameters
> Unlimited fire mode: continuously generate new packets with random source IP
> Burst: 100,000 (1M packets/s firing scenario)
> Execution CPU: single-core mode fixed
  Client Attack Profile
Measurement Objective
Performance Analysis Environment (Benchmark Variables)

## Slide 31
Performance Results: Dynamic Spinlock

## Slide 32
  __nf_conntrack_confirm CPU cost decreased by 1.84% → Reduced lock contention on the connection confirmation path.
  __nf_conntrack_find_get CPU cost decreased by 0.41% - → Shortened lock wait time during existing connection lookup.
  Dynamically allocated locks distribute contention effectively → Overall performance improvement in key functions.
Lock Contention Mitigation Effects
  vp_notify increased by more than 1.6× → Longer spin waits under dynamic spinlock caused more frequent Guest ↔ Host notifications.
  Lock acquisition failures → relax/yield operations in VMs lead to increased hypervisor (Host-OS) involvement.
  In bare-metal environments, this overhead does not occur → greater performance gains expected on physical servers.
Notes (Virtualized Environment)
Performance Results: Dynamic Spinlock

## Slide 33
Performance Results: Per-Bucket Lock

## Slide 34
  vp_notify decreased by 11.37% → Efficient lock handling significantly reduces Guest–Host communication overhead, which was the main bottleneck in virtualized environments.
  __default_idle_call increased by 8.98% → CPU resources were saved and transitioned into idle state → better system efficiency.
  __nf_conntrack_confirm decreased by 1.24% → Reduced overhead during new connection confirmation → improved concurrency.
Lock Contention Mitigation Effects
  __nf_conntrack_find_get increased by 0.59% → Due to reduced noise (e.g., vp_notify), more CPU cycles are now spent on lookup operations.
  Per-bucket lock distribution improves overall system stability and reduces contention.Even in virtualized environments, performance improvement is consistent → Greater stability compared to dynamic spinlock approach.
Detailed Analysis
Performance Results: Per-Bucket Lock

## Slide 35
Dynamic Spinlock
  Both methods reduce the CPU cost of __nf_conntrack_confirm, demonstrating mitigation of lock contention on the new-connection confirmation path.
Common Findings
Per-Bucket Lock
  __nf_conntrack_confirm: ↓1.84%p
  __nf_conntrack_find_get: ↓0.41%p
  vp_notify: ↑16.16%p
  default_idle_call: ↓9.67%p
Performance Metrics
  __nf_conntrack_confirm: ↓1.24%p
  __nf_conntrack_find_get: ↑0.59%p
  vp_notify: ↓11.37%p
  default_idle_call: ↑8.98%p
Performance Metrics
  Dynamically adjusts lock array size to optimize for CPU count and hash table size.
  However, in virtualized environments, longer spin-waits cause increased Host-OS traps
  → significant vp_notify overhead.
  → Works efficiently on bare-metal systems.
Characteristics
  Each bucket owns its own lock → fundamentally distributes contention.
  Even in VM environments, lower vp_notify overhead yields stable performance.
  Drastically reduces Guest-Host communication cost.
Characteristics
Performance Results: Per-Bucket Lock

## Slide 36
Conclusion
The primary performance bottleneck in the Netfilter/Conntrack pipeline is lock contention
Under high-load environments, global lock array contention is a major root cause of performance degradation.
Maintains stability even in virtualized environments and offers superior lock distribution efficiency.
In VMs, increased vp_notify overhead reduces benefits,
whereas in bare-metal systems, it remains effective.
Per-Bucket Lock provides the most consistent improvement
Dynamic Spinlock is suitable for physical servers

## Slide 37
THANK YOU
THANK YOU
TEAM 3